## Slide 1
LCA XV
Jacqueline Ebner
Ph.D. Candidate
Rochester Institute of Technology
Golisano Institute for Sustainability
May 4, 2015
Climate change impacts of retail food waste treatment options based upon substrate characteristics

## Slide 2: Motivation
Much has been done to analyze the GHG impacts of MSW treatment waste
Some studies have looked at constituents of MSW including food scraps
However, resources leave the food supply chain (FSC) at virtually every stage with varying characteristics
Recently several US cities and state have restricted landfilling of food waste. These regulations often target high generators such as supermarkets and large institutions where source separated food waste or categories of food waste are generated
In addition to having unique characteristics, commercial food wastes often have additional options for treatment vs MSW
The objective of this study is to develop a model for assessing greenhouse gas impacts associated with waste treatment pathways based upon FSC resource characteristics.

## Slide 3: Goal, scope and assumptions
Objective to compare the effect of substrate composition on Climate Change impacts for various treatment pathways
Gate to grave-
  Does not include transportation of the food waste to the treatment facility
  Return to ecosphere 100 year impact
Climate change impact- GWP 100 yr AR5 IPCC
Functional unit is 1t FSC resource
Independent of co-product
  External motivation to co-process
  Synergistic or antagonistic effects are within uncertainty range
  Benefits or impacts due to avoided treatment of a co-constituents (ie. Manure) remain associated with that constituent and are not considered
System is expanded to consider displacement of co-products
Ignores capacity contraints (ie. C/N ratio, soil nutrient, animal tolerance, etc.)

## Slide 4: Feedstock and treatment pathways
Food waste categories:
  Baked goods
  Canned goods
  Coffee
  Fresh Produce
  Breakfast cereals
  Grains
  Yogurt and frozen deserts
  Post Consumer
  Prep Waste
  Apple Pomace
  GTW
  Grape Pomace
  Whey
  Cannery waste
Waste treatment:
  Landfill
  Anaerobic digestion-
  Compost- no displaced
  Direct animal feed
  Direct land application
  Public waste water treatment
Retail and Commercial
Sector

## Slide 5: Methodology
A model was developed to estimate lifecycle GHG impacts for each treatment pathway
Based upon the input feedstock characteristics :
  Solids content (TS)
  Volatile solids content (VS)
  Bio-methane potential (Bo)
  Extent of biodegradation (fd)
  Nitrogen content (TKN)
  Composition (CF, CP, carbohydrate)
  Initial Carbon content* (kgC/kgFW)
  Lo*- m3CH4/t FW
  TDN *-(% total digestable nutrients)
  *derived
* derived
Module | Theoretical Basis
Landfilling | LandGEM,EPA LMOP
AD | Ebner et al., 2015
Compost | Boldrin, 2009
Animal Feed | NRDC, 2001

## Slide 6: Background
Bernstad, et al., 2012 reviewed 25 LCAs of food waste treatment alternatives and observed wide variation in results for climate change impact.
They attributed a large portion of the differences to system boundary settings and methodological choices while also acknowledging the impact of the characteristics in treated waste.
In order to provide a comparative analysis of the impact of FSC resource characteristics we must ensure consistent boundaries and methodologies
  Losses during collection, storage and pretreatment – not included at this time
  Consistent and realistic treatment of impacts from production and use of substituted goods (ie: energy, resources, nutrient recovery, carbon sequestration)

## Slide 7: Substituted Systems
Grid electricity (landfill/AD) displaces non-baseload emissions (Egrid,2010)
Soil amendment:
  Baselines
    AD –non-separated effluent land applied to displace inorganic fertilizer based upon N requirement (Ebner, 2015)
    Compost –21% peat, 18% fertilizer (Anderson, 2010)
  Error bars examine impact of
    No displacement
    Fertilizer displacement (AD, Compost)
    Peat displacement (Compost)
Included:
  Displaced, production, application, carbon sequestration, nutrient provision
Does not include at this time:
  Other soil improvements- yield, microbial activity, erosion, water retention, weed control, C in depleted soils

## Slide 8: Feedstock characteristics
Substrate | %TS (TS/FW) | %VS/ TS | TVS (VS/FW) | Bo (ml/g VS) | Lo (m3/MT) | TKN (mg/kg) | % ash/TS | % crude fat /TS | % crude protein /TS | % carbohydrate /TS | extent of degradation | Initial C
Baked goods | 91.60% | 97.90% | 88.90% | 465.30 | 413.66 | 14656 | 3% | 11% | 10.% | 76% | 94% | 435.77
Canned goods | 10.50% | 90.70% | 14.30% | 435.97 | 62.34 | 2520 | 9% | 2% | 15% | 74% | 98% | 44.52
Coffee | 29.30% | 99.30% | 30.30% | 365.25 | 110.67 | 7970 | 1% | 4% | 17% | 79% | 80% | 138.36
Fresh produce | 7.70% | 93.30% | 91.10% | 418.05 | 380.84 | 1232 | 7% | 0% | 10% | 82% | 98% | 32.15
Post consumer | 46.60% | 97.10% | 7.10% | 483.42 | 34.32 | 13421 | 3% | 19% | 18% | 61% | 88% | 239.18
Prep waste | 14.30% | 100.00% | 3.40% | 252.29 | 8.58 | 458 | 0% | 3% | 2% | 82% | 56% | 56.94
Breakfast cereal | 92.70% | 95.00% | 29.10% | 361.82 | 105.29 | 16315 | 5% | 2% | 11% | 82% | 82% | 406.29
Salad mix | 3.80% | 90.60% | 45.20% | 375.37 | 169.67 | 1398 | 11% | 2% | 23% | 66% | 90% | 16.37
Grains | 92.40% | 97.80% | 90.40% | 318.40 | 287.84 | 17741 | 2% | 1% | 12% | 85% | 74% | 415.07
Yogurt and frozen deserts | 30.90% | 97.90% | 9.60% | 454.21 | 43.60 | 6922 | 2% | 5% | 14% | 79% | 99% | 143.38
Solids content ranged from near 4% to 92%
Bio-methane potential ranged from 250mlCH4/gVS to 483mlCH4/gVS
Most substrates were high in Carbohydrate content (60%-85%)
Most highly degradable (74% -99%)
TKN ranged from about 500mg/kg to 1800mg/kg
Solids content had a large influence on Initial C/t and Lo (m3/t)

## Slide 9
Chart: kgCO2e/t
| Salad mix | Fresh produce | Canned goods | Prep waste | Coffee | Food waste | Yogurt and frozen deserts | Post consumer | Baked goods | Unsweetened dry goods | Sweet dry goods
Animal Feed | -14.8153 | -41.2045 | -56.188 | -71.0568 | -44.7975 | -183.4711 | -219.6837 | -284.9917 | -623.2207 | -522.7091 | -566.9256
AF.NormTS
AD.ADnetEmissions
AD.EMDigester
AD.EMStorage
AD.EMLandApp
AD.EMCstorage
AD.EMdisplacedFertilizer
AD.NormTS
AD | 24.648 | 23.2918 | 26.9779 | 9.5504 | 31.0792 | 36.5057 | 35.0737 | 4.2259 | -4.6379 | 37.9159 | 36.5352
ADf.EMDigester
ADf.EMStorage
Baseline Results
Notes: Net impact ranged from 2322kgCO2e/t for landfilling of baked goods to -154kgCO2e/t for composting of salad mix with peat displacement
Landfill consistently the highest impact but varied by orders of magnitude (salad mix 83 kgCO2e/t)
Ranking of other pathways varies and compost use has a large impact

## Slide 10: Compost and AD impacts and the influence of use of co-product
Chart: 
| Salad mix | Fresh produce | Canned goods | Prep waste | Coffee | Food waste | Yogurt and frozen deserts | Post consumer | Baked goods | Unsweetened dry goods | Sweet dry goods
AF.NormTS
AD.EMDigester
AD.EMStorage
AD.EMLandApp
AD.EMCstorage
AD.EMdisplacedFertilizer
AD.NormTS
AD | 24.648 | 23.2918 | 26.9779 | 9.5504 | 31.0792 | 36.5057 | 35.0737 | 4.2259 | -4.6379 | 37.9159 | 36.5352
ADf.EMDigester
ADf.EMStorage
ADf.EMLandApp
ADf.EMCstorage

## Slide 11: Conclusions and limitations
Use of food scraps as a proxy for all FSC resources may lead to large errors in estimating GHG impacts
Landfill showed highest impact and Animal feed lowest across all feedstocks, TS had a large influence
Diverting feedstock with large landfill impacts (high Lo) to other pathways can have a large impact (i.e. 2946kgCO2e/t stale baked goods)
Diverting food from feeding animals to alternative pathways may increase net GHG impacts
Alternative pathways (AD, Compost) were influenced by TS as well as other feedstock parameters
Co-product influences net impact of alternative pathways
There is significant variation and uncertainty in modeling

## Slide 12: Future Work
Monte Carlo simulation to quantify and understand uncertainty
Integrate industrial food waste feedstocks and pathways (ie. WWTP)
Implement additional “application states” (ie. AD w/ separation and composted digestate, diversion to feed swine, recycling of packaging, etc.)
Include other soil amendment benefits
  Understanding of the difference in long term carbon storage among alternative soil amendments (fertilizer, untreated manure, digested manure, composted untreated FW, FW digestate)

## Slide 13: Acknowledgement
Funding for this research program was provided by the New York State Pollution Prevention Institute through a grant from the New York State Department of Environmental Conservation. Any opinions, findings, conclusions or recommendations expressed are those of the author(s) and do not necessarily reflect the views of the Department of Environmental Conservation

## Slide 14: Back up

## Slide 15: Simplification of model formulations
AD= 19 -1.11*Lo + 455*TVS + .0074*TKN – 1.46*InitialC + 1.46*InitialC*fdeg
CMLM = 38_ 5.95TKN*TS -2.13Initial C +2.566*InitialC*fdeg
LFLM=24.979 +9.281*Lo - InitialC * fdeg

## Slide 16: Impact of carbon sequestration

## Slide 17: “Carbon Sequestration”
Long term storage or binding of carbon so as to remove it from the atmospheric CO2 cycle (>100yrs)
ILCD recommend no carbon storage as a default
  Affected by C/N ratio, temperature and humidity
However included in several studies
  Landfill- (Barlaz et al, 1998) stored C remaining after anaerobic degradation
  CSL= CInitial (kg/t) * (1-fd)
  Where: fd= Measured bio-methane yeild
      Theoretical bio-methane yeild
  AD/Compost- (WARMv13) C in non-reactive humus after DOC removal
  CSi=CInitial (kg/t) * (1-fd)*(1-fi)
Where fi is a correction factor
  fc=0.8 (8% of C applied (Boldrin,2009) and 3% of Initial C (Bernstadt, 2012))
  fAD= 0.6 (10% of C applied (Boldrin, 2009) and 6% of initial C (Baky and Eriksson, 2003 )

## Slide 18: Uncertainty

## Slide 19: Anaerobic Digestion
CO2 fossil + upstream
Digester Operation
Digestate Land Application
Digestate Storage
CH4
Displaced Grid Electricity
Displaced inorganic Fertilzer
AD
N2O
N2O
CO2 fossil + upstream
CH4
N2O
Relevant Emission Factors | units | Nominal | Lower | Upper | Source
Grid electricity displacement | kgCO2e/ MWh | -537.36 | -918.79 | -537.18 | Egrid, 2012
Methane conversion factor | % | 0.84 | 0.7 | 1 | Ebner et al, 2014
Methane leaks | % methane utilized | 0.03 | 0 | 0.1 | Ebner et al., 2014
Methane incomplete combustion factor | % methane utilized | 0.005 |  |  | Dressler, 2012
Conversion Efficiency | MWh/t | 4.19 | 3.23 | 4.70 | Ebner et al, 2014
Parasitic load | % KWh generated | 0.12 | 0.1 | 0.2 | Ebner et al, 2015
VS destruction | % | 0.55 | 0.4 | 0.7 | Ebner et al., 2014
Effluent residual methane factor | m3CH4/kgVS | 0.054 | 0.004 | 0.074 | Ebner et al., 2014
Direct N2O emission factor | kgCO2e/t | 0.005 | 0.0025 | 0.01 | IPCC protocol, EF3=0.005
Indirect N volitilization factor | KgNvol/kg N | 0.26 | 0.05 | 0.5 | FracGASMS=0.26
Indirect N2O-N from NH3 | Kg N2O-N/kg N | 0.01 | 0.002 | 0.05 | IPCC, EF4=0.01

## Slide 20: Landfill module
Landfill
Decay emissions
Landfill Operation
Displaced Grid Electricity
CH4 released
COe2 fossil + upstream
COe2 fossil + upstream
CH4 captured
Electricity generation
Flare
Relevant Emission Factors | units | Nominal | Lower | Upper | Source
Provision of diesel | kgCO2e/L diesel | 0.45 | 0.4 | 0.5 | Fruergaard et al. (2009)
Diesel combustion | kgCO2e/L diesel | 2.72 |  |  | GREET 2014 (2010 dataset)
Grid electricity displacement | kgCO2e/MWh | -537.36 | -918.79 | -537.18 | Egrid, 2012
Diesel use at landfill | L/t | 5.83 | 4 | 10 | WARM v.13
Factor of oxidation | % | 0.1 | 0.1 | 0.35 | EPA biogenic
Gas Capture factor (GC) | % | 1 | 0.85 | 0.9 | WARM
Heat rate of LF to E conversion | btu/kwh | 11700 | 10663 | 13123 | EPA 2013
Landfill Capacity Factor | % | 0.85 | 0.8 | 0.9 | WARM v13, EPA 2013
Max landfill capture efficiency | % | 0.9 | 0.85 | 0.95 | Levis and Barlaz, 2011
Correction factor | fraction | 1 | 0.7 | 1 | Cho et al., 2012
Decay rate constant (k) | yr-1 | 0.144 | 0.10 | 0.229 | Levis and Barlaz, 2011

## Slide 21: Carbon storage

## Slide 22: Land Application

## Slide 23: Compost
N2O
Compost
Compost Operation
Displaced peat production and application
CO2 fossil + upstream
Decay emissions
CO2 fossil + upstream
CH4
Displaced inorganic fertilizer production and application
landscaping
use
Horticulture

## Slide 24: Impact of CS assumptions